## Slide 1: Chapter 8
Image Restoration

## Slide 2: Contents
Introduction
Noise
Cleaning Salt and Pepper Noise
Cleaning Gaussian Noise
Removal of Periodic Noise
Inverse
Weiner Filtering

## Slide 3: Introduction
Concerns removal or reduction of degradations that occurred during image acquisition
  Noise: errors in pixel values
  Optical effects: out of focus blurring
  Blurring due to camera motion
Image restoration is one of the most important areas of image processing
Focus: techniques for dealing with restoration

## Slide 4: Noise
Definition: any degradation in the image signal, caused by external disturbance
Cleaning an image corrupted by noise is an important area of image restoration
Look at 4 different noise types:
  Salt and Pepper Noise
  Gaussian Noise
  Speckle Noise
  Periodic Noise
Clean using spatial filtering techniques, local degradations
Clean using frequency domain filtering, global effect

## Slide 5: Salt & Pepper Noise
A.k.a. – impulse noise, shot noise, binary noise
Cause
  sharp, sudden disturbances in the image signal
Appearance
  Randomly scattered white or black (or both) pixels over the image

## Slide 6: Salt & Pepper Noise

## Slide 7: Gaussian Noise
Definition: idealized form of white noise that is normally distributed
Can be modeled by random values added to an image
Cause:
  Random fluctuations in the signal
Example:
  Television slightly mistuned to a particular channel

## Slide 8: Gaussian Noise

## Slide 9: Speckle Noise
A.k.a. – multiplicative noise
Can be modeled by random values multiplied by pixel values
Major problem in some radar applications

## Slide 10: Speckle Noise

## Slide 11: Gaussian vs. Speckle Noise

## Slide 12: Periodic Noise
Occurs when an image is subject to a periodic disturbance
  Effect of bars over the image
Figure 8.3: The gull image corrupted by periodic noise

## Slide 13: Periodic Noise
Neither function imnoise or random_noise has a periodic option, but it is quite easy to create such noise, by adding a periodic matrix (using a trigonometric function) to the image.

## Slide 14: Cleaning Salt & Pepper Noise
Low Pass Filtering
  Pixels corrupted by salt & pepper noise are high frequency components of an image, can expect a low pass filter should reduce them
Figure 8.4: Attempting to clean salt and pepper noise with average filtering

## Slide 15: Cleaning Salt & Pepper Noise
Median filtering
  Almost tailor made for removal of salt & pepper noise
  example of a non-linear spatial filter
  Using 3 x 3 mask, output value is median of values in the mask
  Very large or very small values (noisy values) end up at the top or bottom of the sorted list
  Replaces noisy value with one closer to its surroundings

## Slide 16: Cleaning Salt & Pepper Noise

## Slide 17: Cleaning Salt & Pepper Noise
Figure 8.5: Cleaning salt and pepper noise with a median filter

## Slide 18: Cleaning Salt & Pepper Noise
MORE NOISE!!!!

## Slide 19: Cleaning Salt & Pepper Noise
Figure 8.7: Cleaning 20% salt and pepper noise with median filtering

## Slide 20: Cleaning Salt & Pepper Noise
Rank-Order Filtering
  Nth value of ordered list is chosen, for some predetermined value of n
  When to use Rank-Order filtering instead of median filtering?
    When using a median filter over non-rectangular masks

## Slide 21: Cleaning Salt & Pepper Noise
Rank-Order Filtering

## Slide 22: Cleaning Salt & Pepper Noise
Rank-Order Filtering

## Slide 23: Cleaning Salt & Pepper Noise
Outlier Method
  treat noisy pixels as outliers
    Outliers are pixels whose gray values are significantly different from those of their neighbors
  Approach:
    Choose a threshold value D
    For a given pixel, compare its value p with the mean m of the values of its eight neighbors
    If |p – m| > D, then classify the pixel as noisy
    If the pixel is noisy, replace its value with m
  Choosing the right D value is essential!

## Slide 24: Cleaning Salt & Pepper Noise
Outlier Method

## Slide 25: Cleaning Salt & Pepper Noise
Create a matrix of 1's over noisy pixels
If a pixel is noisy (r = 1), use the new pixel value (average of neighbors stored in gspa), but if it is not noisy (r = 0), use the original pixel value (stored in gsp)

## Slide 26: Cleaning Gaussian Noise
Image Averaging
  Sometimes we have different copies of an image corrupted with Gaussian noise
  Example:
    Satellite imaging
      Satellite passes over the same spot many times, taking pictures, many different images of the same place
    Microscopy
      Many different images of the same object are taken
  When these types of problems occur, its very easy to take the average of all the images

## Slide 27: Cleaning Gaussian Noise
Figure 8.9: Image averaging to remove Gaussian noise

## Slide 28: Cleaning Gaussian Noise
Average Filtering
  If Gaussian noise has mean 0, expect average filter to average noise to 0
    Larger the size of filter mask, the closer to 0
  Unfortunately this tends to blur an image
  Sometimes the tradeoff of blurring for noise reduction is worthwhile

## Slide 29: Cleaning Gaussian Noise
Figure 8.10: Using averaging filtering to remove Gaussian noise

## Slide 30: Cleaning Gaussian Noise
Adaptive Filtering
  Class of filters that change their characteristics according to the values of the grayscales under the mask
  Cleans Guassian noise by using local statistical properties of the values under the mask
  Minimum mean-square error filter
    Non-linear spatial filter implemented by applying a function to the gray values under the mask
    Name reflects that this filter attempts to minimize the square of the difference between the input and output images

## Slide 31: Cleaning Gaussian Noise
Adaptive Filtering
We will use the wiener filter (developed by Norbert Wiener in 1942), which can take an optional parameter indicating the size of the mask to be used. The default size is 3 × 3. We shall create four images:

## Slide 32: Cleaning Gaussian Noise
Figure 8.11: Examples of adaptive filtering to remove Gaussian noise

## Slide 33: Cleaning Gaussian Noise
Figure 8.12: Using adaptive filtering to remove Gaussian noise with low variance

## Slide 34: Removal of Periodic Noise
Periodic noise occurs when imaging equipment is subject to electronic disturbances of a repeating nature
Figure 8.13: The gull image (a) with periodic noise and (b) its transform

## Slide 35: Removal of Periodic Noise
Extra 2 spikes in 8.3(b) correspond to the added noise
In general, the tighter the period of the noise, the further from the center the spikes will be
  Because small period corresponds to high frequency
Methods to remove spikes
  Band reject filtering
  Criss-cross filtering
Figure 8.13: The gull image (b) its transform

## Slide 36: Band Reject Filtering
Figure 8.14: Removing periodic noise with a band-reject filter

## Slide 37: Band Reject Filtering
Figure 8.15: Removing periodic noise with wider band-reject filters

## Slide 38: Criss-Cross Filtering
A criss-cross filter sets the rows and columns of the transform that contain the spikes to zero
  The more rows and columns of the transform that are set to zero, the better the noise reduction
Figure 8.16: Removing periodic noise with a criss-cross filter

## Slide 39: Inverse
We can perform filtering in the Fourier domain by multiplying the DFT of an image by the DFT of a filter
  Direct use of convolution theorem
Thus
  X is DFT of image
  F is DFT of filter
  Y is DFT of result
With this, if given Y and F, we should be able to retrieve X

## Slide 40: Inverse
1st attempt at inverse filtering
  NO improvement! Now what?
Figure 8.17: An attempt at inverse filtering

## Slide 41: Inverse
Why no improvement?
  Some elements of Butterworth matrix are very small
  Dividing produces very large values that dominate output
Two steps for improved results
  Apply a low pass filter L to the division:
    Eliminates very low (zero) values
  “Constrained division”: choose a threshold value d, and if |F(i, j)| < d, the original value is returned instead of a division. Thus:

## Slide 42: Method 1
Implementation
  Multiply a Butterworth low pass filter to the matrix
Butterworth cutoff radius
  (a) 40
  (b) 60
  (c) 80
  (d) 100
Low pass filter with cutoff about 60 yields best results
Figure 8.18: Inverse filtering using low pass filtering to eliminate zeros

## Slide 43: Method 2
Implementation
  Make all values of the filter that are too small equal to 1
Butterworth cutoff radius
  (a) d = 0.01
  (b) d = 0.005
  (c) d = 0.002
  (d) d = 0.001
Using a threshold d in the range 0.002 ≤ d ≤ 0.005 produce reasonable results
Figure 8.19: Inverse filtering using constrained division

## Slide 44: Motion Deblurring
Blurring caused by motion
Figure 8.20: The result of motion blur

## Slide 45: Motion Deblurring
Deblurring the image using DFTs
  Divide image transform by the transform corresponding to the blur filter
How?
  Create a matrix corresponding to the transform of the blur
  Divide by this transform
We see poor results because values close to zero dominate the result (use constrained division to clean up the blur)

## Slide 46: Weiner Filtering
Given a degraded image M’ of some original image M and a restored version R, what measure can we use to say whether our restoration has done a good job?
  Want R to be as close as possible to correct image M
  Measure closeness by adding the squares of all the differences
    Goal: Minimize the closeness measure
Weiner filter: a filter that operates on the principle of least squares

## Slide 47: Weiner Filtering
K values
  (a) K = 0.01
  (b) K = 0.001
  (c) K = 0.0001
  (d) K = 0.00001
Note that as K becomes very small, noise starts to dominate the image
Figure 8.22: Wiener filtering